1) Gather all the parts and tools listed in the bom. Should include:

XD87 Kit7:
XD87 PCB board
lower plastic case
upper plastic case
stainless steel frame
90 switches
90 LEDs
micro USB cable

Stabilizers
4 2x sets
1 6.25x set

Keycaps
87 keys, includes all but the numpad

Tools
soldering tool
solder (lead-free)
wire clipper
soldering wick (optional)
case tool (included in XD87 kit)

2) Get an idea of key placement.

The bottom row of keys and the caps lock key can have different placements, so you need to map out your placements first. Place the PCB on a flat surface, then the steel frame on top of that. Then, take the bottom row of key caps and the caps lock key and space them out on top of the frame. Take a switch and determine what position each switch will have to be in for each key. Note them down and mark them on the plate.

3) Assemble and install the stabilizers.

Place the PCB on a flat surface. The backspace, enter, and two shift keys require a 2x set of stabilizer, and the space bar will require the 6.25x. The 2x sets are predetermined where they go. The spacebar has a few options in placement, which should be determined in step 2.

Each stabilizer has 5 parts. 2 mounts, 2 stems, and a metal bar. Insert the stems into the mounts, then the bar into both to connect them. The bar should snap into place.

Install each stabilizer set into the PCB board at the backspace, enter, two shift, and spacebar locations. The holes for the stabilizers are unique and are appropriately spaced out. They may require a lot of force to snap them into the PCB.

4) Insert the switches

Place the metal plate on top of the PCB. The holes in the plate should match up with the installed stabilizers. If not, remove them and repeat step 3.
Each switch has 5 pins: 3 black plastic and 2 copper ones. Take each switch and insert them into the plate and PCB. The center black plastic pin needs to be pushed into the PCB, which requires a bit of force to get in. Upon snapping it in, the two other black pins should be pushed through as well. This will also snap in the switch into the plate as well. Note that a few switches may come with a bent copper pin, so be sure to bend it straight before snapping in the switch. The two copper pins should be slightly pushed through the PCB.

For the caps lock and bottom row of keys, double check the keycap spacing before snapping in the switches.

Note: not every key is used in the XD87 kit. Top row, second key from the left is not used, nor are the two keys to the left and right of the up key. If these switches are installed, they will be covered up by the top case.

5) Soldering the switches

Use the soldering tool and lead free solder to create a connection for every copper switch lead.

6) Insert LEDs

Take each LED bulb and insert each one through each switch. Note that on the back of the PCB, the LED stems come out of holes that have a circle or square border. The square is for the positive end, and the circle is for the negative end. The longer LED pin is the positive, so ensure each LED is correctly lined up. Bend the pins to hold the LEDs in place for when you turn the PCB over.

Note that the caps lock key can have an LED inserted on the side.

7) Solder the LEDs

Use the wire clipper to clip off one pin of each LED, then solder each clipped pin. Then you can clip the other pin and solder those.

8) Place keycaps on to the switches

Press each keycap in their appropriate place on top of each switch. This step can be skipped and done after step 9.

9) Insert assembly into the case

Place the assembly into the lower plastic case; be sure to connect the PCB to the hot swap board as well. Now place the upper place case on top. Ensure both of the cases are properly snapped into each other.

On the underside, connect the usb cable into the port.

10) Flash and test the keyboard.

Connect the keyboard to a computer and flash your new keyboard.