Notes

PCB

-stands for printed circuit board

-is the electronic part of the keyboard that communicates with the computer

-common sizes are 60%, 90%, and 100%.
-60% is letters, top numbers, shift, alt, ctrl, enter, backspace, caps, tab. Often programmed to	give keys additional functions to make up for missing keys.
-90% includes the above plus arrow keys, F row, and the 6 keys above the arrow keys
-100% includes all the above plus the numpad

-each key position has 2 holes at the top. One is shaped like a square, the other a circle. This is for the LEDs. Square = positive, circle = negative

-most guides and homemade keyboards are with 60% boards.

Switches

-3 types: linear, tactile, clicky
-clicky is the loudest and has a distinct clicking noise
-tactile is more quiet and has a bump in the stem to provide resistance that’s felt at acctuation
-linear is most quiet, has no resistance or interference. Can still make noise when bottomed out.	Cherry MX red is the most common/popular choice.

-can be 3 pin or 5 pin. Always choose 5 pin as extra pins can be clipped off
-3 pin is for mounting on a plate
-5 pin is for mounting on a PCB

-will additionally have holes to allow LEDs to be inserted

-most boards will require soldering to add on switches

Keycaps

-a profile of a keycap determines the shape. A profile can have several different shapes depending on what row the keycap will be on.

-most common profiles are OEM and cherry

-most common material are ABS and PBT

-can be made doubleshot, which makes the keys thicker and heavier

-can be backlight by an LED on the switch. This shines a light through the text on the key

Lighting

-if a keycap supports backlighting, then an LED can be mounted on

-most PCB can support board backlighting. Some come with lights, while others require soldering an LED light strip.

-for single LEDs that are inserted into the switches, the longer stem is for positive, shorter is negative