I2C-HID keyboard

Using hid-over-i2c-protocol-spec-v1-0.docx (Microsoft I2C-HID documentation), and I2C-HID linux driver sources (https://github.com/torvalds/linux/blob/master/drivers/hid/i2c-hid/i2c-hid-core.c).
Main hardware I2C-HID requirements.
1. Two I2C lines, SCL and SDA (inouts). I2C must work in slave mode.
2. Interrupt line (output).

Main software I2C-HID requirements.
1. Two descriptors (I2C-HID descriptor and HID report descriptor). These descriptors are transmitted to HOST after receiving appropriate commands.
2. Interrupt logic. If device has non-readed input report, it generates interrupt. Interrupt is de-asserted after input report reading. Also interrupt with empty input report (length is zero) is generated after reset. Device can have a queue of input reports.
3. Command and output report processing logic. Mandatory commands: RESET, GET_INPUT_REPORT, SET_OUTPUT_REPORT, SET_POWER. Also HOST can send I2C-HID or HID report descriptor request. Now SET_POWER command is ignored (if device ignores this command, I2C-HID logic is not uncorrect). Maybe in future some energy saving mode will be realized in FPGA. Other commands are supported.
4. Reports and report descriptor are the same as in USB HID. Now default keyboard reports are used. Input report — 8 bytes, byte 0 — modifier keys (bit 0 — left ctrl, bit 1 — left shift, bit 2 — left alt, bit 3 — left meta (win), bits 4-7 — same right keys), byte 1 is always zero, bytes 3-7 — pressed key codes (zeros if no keys pressed). Output report — 1 byte (bit 0 — NumLock LED, bit 1 — CapsLock LED, bit 2 — ScroolLock LED).

Matrix keyboard algoritm.
Now device has only polling keyboard control mode. It means that device sets one active row in one cycle and reads columns state. At next cycle next row will be active etc.

More about I2C transactions (see I2C-HID requirements):
Device can receive and process 7 different I2C-HID packets:
1. 01 00 — I2C-HID descriptor request. 01 00 — 16 bit adress of I2C-HID descriptor, LSB first (all 16-bit adresses and
 in I2C-HID are LSB first). This adress can be modified in linux driver settings
2. 02 00 — HID report descriptor request. 02 00 — HID report descriptor adress, from I2C-HID descriptor
3. 03 00 — get input report (from register). 03 00 — input report adress, from I2C-HID descriptor
4. 05 00 00 01 — RESET command. 05 00 — command adress, from I2C-HID descriptor, 00 01 — special code for RESET command (see documents)
5. 04 00 01 00 XX — set output report (to register). 04 00 — output report adress from I2C-HID descriptor, 01 00 — output report length, XX — report byte (LED state)
6. 05 00 10 02 06 00 — get input report (command). 05 00 — command adress, from I2C-HID descriptor, 10 02 — GET_INPUT_REPORT command code, 06 00 — data adress, from I2C-HID descriptor
7. 05 00 20 03 06 00 01 00 XX — set output report (command). 05 00 — command adress, from I2C-HID descriptor, 20 03 — GET_INPUT_REPORT command code, 06 00 — data adress, from I2C-HID descriptor, 01 00 - output report length, XX — report byte (LED state). Has the same effect as number 5.

Device can transmit 3 different I2C-HID packets:
1. 1E 00 … (30 bytes) — I2C-HID descriptor. Code 0 in firmware. Sets after receiving packet No.1
2. 05 01 … (63 bytes) — HID report descriptor. Code 1 in firmware. Sets after receiving packet No.2
3. 0A 00 XX XX XX XX XX XX XX XX (10 bytes, 2 bytes of length (calculated sum of report len + length field len) + 8 bytes of report) — input report. Code 2 in firmware. Sets after interrupt asserts, after transmitting some other packet, or after receiving packets No. 3 or 6. 0A 00 — length, XX (8 bytes) — default keyboard input report.

I2C-HID keyboard Ice40 modules description:

1. descriptors.v (input CLK, input DESC_TYPE, input [6:0] ADR, output [7:0] VAL)
ADR — adress of current byte in descriptor (first adress is 1, not 0, because it is simpler in realization)
DESC_TYPE — 0 for i2c-hid descriptor and 1 for hid report descriptor
CLK — clock for RAM
VAL — current byte of current descriptor at the current adess.
There are two descriptors in one RAM block. Bit 7 of RAM adress — DESC_TYPE, bits 6-0 — ADR. No other logic is used.

2. i2c_slave.v (input CLK, input RESET, input SCL, inout SDA, output IS_TRANSMISSION, output IS_READ, output IS_ACK, output WR, output [7:0] RECEIVED_BYTE, input [7:0] BYTE_TO_TRANSMIT)
CLK — clock for this module (module tacts from main clk, not from i2c_clk)
RESET — reset wire for this module, for write to some registers default values. If this wire is 0, reset occurs. If 1 — normal work
SCL, SDA — i2c lines, clock and data
IS_TRANSMISSION — value of this wire is 1 after i2c start condition, and is 0 after i2c end condition. After repeated start value is 0 in one tact, and is 1 after this tact (for top module, it can find end of packet)
IS_READ — wire is 1, if i2c master reads data from device, and is 0, if master writes data to device
IS_ACK — wire is 1 in nine bit (ack bit). Only for debug i2c logic
WR — signal to write next byte (if IS_READ == 1) or to read current byte (IS_READ == 0). Is used in top module
RECEIVED_BYTE — top module can read this byte after WR signal (if IS_READ == 0)
BYTE_TO_TRANSMIT — top module write this byte after WR signal (if IS_READ == 1)

Module has default i2c logic. Clock stretching is not supported beacuse it is not needed. Two simple filters are used in this module (for SCL and SDA lines).

3. matrix_kbd.v (input CLK, input RESET, input FREEZE, inout [15:0] ROWS, input [7:0] COLUMNS,
input [3:0] REPORT_ADRESS, output [7:0] REPORT_DATA, output INT)
CLK — clock for this module
RESET — reset wire for this module. Module will write default values to it`s RAM after reset (now ~150
tacts or ~12.5 mks) and then will work in normal mode
FREEZE — if FREEZE == 1, keyboard pooling freezes
ROWS — 16 row lines of keyboard
COLUMNS — 8 column lines of keyboard
REPORT_ADRESS — number of current byte of current input report. For top module
REPORT_DATA — value of current byte of current report. For top module. Is avaluable if there is no
report modification process.
INT — signal to top module, means that report is modified. Now report if modified, then int signal
generated, then top module can read new report
Module now has only polling keyboard control mode. Keyboard module searches pressed/released keys
and then modifies input report (adds key code to report or deletes this code). If report modified,
generated interrupt signal for top module.

4. ram.v (input clk, wen, input [8:0] waddr, input [7:0] wdata, input [8:0] raddr, output [7:0] rdata)
CLK — clock for RAM
WEN — write enable wire
WADDR — RAM adress for write operation
WDATA — data for write operation
RADDR — adress of readed data in RAM
RDATA — read data from RAM

Module is RAM memory block only, when project is built, this module is transformed to SB_RAM. This syntax is recommended by Clifford Wolf (https://stackoverflow.com/questions/41499494/how-can-i-use-ice40-4k-block-ram-in-512x8-read-mode-with-icestorm).

Note: Write and read operations are not instant. Only one write and only one read operation can be used in one tact, results of operations are avaluable in next tact. Please use first 256 adresses (0-255), some problems can occur with adresses 256-511.

5. simple_filter.v (input CLK, input RESET, input IN, output OUT)
CLK — clock for this module
RESET — reset signal for this module
IN — input wire
OUT — output wire
Module is very simple filter. If input line state is changed, module waits 7 tacts and then changes output
line (if input line is in changed state after 7 tacts), or not changes output line (if input line is in not
changed state). Needed for long i2c physical lines (with some interferences) or if i2c master has not
correct realization (ft2232 read fxn from ftdi drivers has excess pulse for example). This module is used only in i2c_slave module.